## Slide 1
Bachelor Thesis Project
Techno-Economic Analysis of Sabatier Reaction
Under the supervision of
Dr. Koustuv Ray
Department of Chemical Engineering
Indian institute of Technology, Kharagpur
Arghadeep Biswas
21CH30049

## Slide 2
Power-to-Gas
Three Main Processes
C
Capture Technology
Oxy-Fuel Combustion System
Pre-Combustion System
Post Combustion System
Water Electrolysis
Based on Splitting water molecules
Alkaline Water Electrolysis mostly used
Catalytic Methanation
CO2 + H2
(CO2)ads
(HCO3)ads
(HCOO)ads
CH4
(CO2)ads
(HCO3)ads
(C)ads
H2
Direct methanation of CO2
CO2 + H2
CO as intermediate
Madeddu et al.

## Slide 3
SCOPE
Streamline techno-economic analysis (TEA) of emerging carbon-utilization technologies
Identify cost and environmental impact hotspots rather than highly precise cost estimates for early stage technologies
Useful for technologies converting captured CO2 and green hydrogen into methane, contributing to India’s commitment to Carbon Neutrality
Helps address uncertainties in cost and environmental impact for technologies in the early stages of development, from idea to pilot trial

## Slide 4
Carbon Capture
Key Steps
Absorption
Preheating
Stripping
Regeneration
Solvent
Flue gas enters the bottom of the absorber column.
Counter current absorption through MEA solvent
Rich CO2 heated through HE1 and HE2
Fed to the second stage of the stripper column
Vapours from reboiler strips CO2
Stripped CO2 goes to a separator to get pure yield
Stripped MEA recycled back to the absorber
Make up water is also add
11 mol % CO2
Rad-Frac based Model
Rad-Frac
based Model
Inspired from CO2 Capture by Reactive Absorption-Stripping Modeling, Analysis and Design by Madeddu et al.

## Slide 5
Electrolysis and Methanation Reactor
H20FEED is fed at 25⁰C and 1 bar
Electrolysis reaction takes place inside the ‘RGibbs’ reactor
H2 produced at the cathode
O2 produced at the cathode
Used as a input to the methanation reactor
Kinetics of ruthenium(Ru) based catalyst was used
Soave-Redlich-Kwong equation of state as property method
Isothermal homogeneous plug flow reactor is used
The following equation reported by P.J. Lunde et al. was used for the temperature dependence
Estimated kinetic parameters(Adopted from LundeWI dataset 2)
Sabatier reaction

## Slide 6
Experimental Plan – Sabatier Reaction
The following process conditions were used to gather kinetically relevant data on CO₂ conversion and CH₄ selectivity: temperature (T) between 250 and 410°C, pressure (P) between 1 and 7 atm, gas hourly space velocity (GHSV) from 3.75 till 10.00 L(STP)/h/g_cat, and a H₂/CO₂ inlet ratio between 1 and 5 mol H₂/mol CO₂ (while maintaining constant CO₂ partial pressure).
. Kinetic input for Sabatier reaction in Aspen plus
GHHLW Adsorption input for forward reaction
GHHLW Adsorption input for reverse reaction

## Slide 7
Simulation Results
Conversion dependence on (a) T, (b) P, (c) GHSV, (d) H2/CO2
(a)
(b)
(c)
(d)
95% CO2
100% H2
Results Summary

## Slide 8
Techno-Economic Analysis
The system consists of three main units
1. Carbon capture system employing MEA as the solvent
2. A plug flow reactor based catalytic methanation using Ru as the catalyst
3. Electrolyser system
Treats the CO2 flows after MEA carbon capture as input
TEA Template
Study components
Goal
Scope
Inventory
Indicator
Interpretation
TEA guidelines
Low technology
readiness level
assessment guidance
Example processes
and placeholder data
Order of magnitude
estimations
Sensitivity and
uncertainty
analysis
Economic and
hotspot analysis
Overview of inputs, outputs and features
Scenario Analysis
Base case: In the default scenario, 10,000,000 kg are produced, average electricity prices and impacts are used, Catalyst A is used
Scenario#1: Renewable Electricity: This first scenario models the use of renewable electricity (50% solar and 50% wind)
Scenario#2: Catalyst B is used in place of catalyst A
Snapshot of Excel Sheet

## Slide 9
Scenario Specification
Catalyst parameters and Reaction energy
Cost parameters
Machine parameters
Inventory
Inventory Parameters
Purchase Equipment Cost
Capital Expenditure CAPEX
For absorber and stripper, equipment costs are calculated

## Slide 10
Operating Expenditure OPEX
Assumptions
Process operating for 90% of the year
Scaling factors are used
Emissions for capital equipment are ignored
Pay-check of debt taken for equipment over 20 years
Pay-check of debt taken for factory taken over 30 years
Indicator Summary
The expected purchase equipment cost was
$22 million
CAPEX – 21.3 M$
OPEX – 35.4 M$
Indicator Calculation

## Slide 11
Sensitivity Analysis
Production Volume(t/year): At 100 million kg per year, cost is down from around $57/GJ to $45/GJ
Electricity cost($/kWh):Varying electricity costs from $0.01/kwh to $0.15/kWh increases manufacturing costs from around $15/GJ to around $85/GJ.

## Slide 12
Uncertainty Analysis
Carbon Dioxide Cost($/year): Varying the carbon Dioxide costs captured directly from the air from $0.05/kg to $0.20/Kg increases the manufacturing costs from around $6.8/Kg to $15/Kg
Water Cost($/year): Varying water cost from $0.0005/kg to $0.0015/kg has a negligible impact on manufacturing costs

## Slide 13
Economic Insights and Recommendation
Insight 1
Insight 2
Recommendation 1
Recommendation 2
Cost of GJ of methane is around $50/GJ
Energy required for process comprises majority (~80%) of the cost
Carbon dioxide is the next largest cost contributor at around 20%
The process is inefficient
Renewable electricity decreases costs to $38/GJ
Use an alternative catalyst has a negligible effect on overall costs
Increasing production volume to 100M kg reduces costs to $45/GJ
Using electricity that costs $0.01/kWh would decrease costs to $15/GJ
Sourcing carbon dioxide at $0.05/kg decrease costs to $45/GJ
Researchers should seek to use the lowest cost possible
Innovating to reduce the costs of hydrogen production help reduce manufacturing cost
Process becomes more economically viable in areas where methane is more expensive
Place where there is cheap electricity
Place where cheap hydrogen can be sourced

## Slide 14
CONCLUSION
Carbon Capture
Capture capture model simulated with 30% MEA conc.
Nearly 85% capture efficiency.
30 KW reboiler Load
Methanation Reaction
Combined with H2 from electrolysis.
Modelled in a plug flow reactor
Conversion varied against temperature, pressure, GHSV, and H2/CO2 ratio
Techno-Economic Analysis
CAPEX and OPEX were analysed
Yearly costs were estimated
Sensitivity and Uncertainty analysis were looked upon
Future Work
Use Aspen Plus dynamics rather than a steady state approach
To not use constant cash flows to get a more realistic approach
Sensitivity and Uncertainty analysis were looked upon
Please refer to the Excel sheet: https://t.ly/UFHzR